## Slide 1
Intelligent Home Security System
Intrusion Detection using Ultrasonic Sensor with Automatic Door Control, Alarm Generation, Cloud Notification & Telegram Alerts
STM32 + ESP32 + Firebase + Telegram

## Slide 2
Project Overview
Objective: Detect intruders using an Ultrasonic Sensor and secure the premises instantly.
•
Lock the door automatically using a Servo Motor.
•
Activate LED and Buzzer during an intrusion.
•
Send instant alerts through Telegram.
•
Store security events in Firebase Realtime Database.

## Slide 3
1. Input & Processing
The HC-SR04 Ultrasonic Sensor detects physical presence.
Data flows directly into the STM32F446RE for real-time edge processing and logic evaluation.
2. Local Output Action
Upon detection, the STM32 triggers immediate local actions.
Servo Motor locks the door, while the LED and Buzzer initiate a high-visibility alarm sequence.
3. Cloud & Connectivity
Alert data is pushed via UART to the ESP32 WiFi Module.
The ESP32 communicates securely with Firebase Database and dispatches Telegram Bot alerts.
System Architecture

## Slide 4
Component | Quantity | Primary Role
STM32F446RE | 1 | Main Controller for logic & actuator handling
ESP32 Dev Board | 1 | WiFi Communication & Cloud Integration
HC-SR04 Ultrasonic | 1 | Intrusion Detection (Proximity)
SG90 Servo Motor | 1 | Automated Door Lock Control
Active Buzzer & LED | 1 each | Local Alarm & Status Indication
Push Button | 1 | Manual System Reset / Override
Complete Hardware Components

## Slide 5
HC-SR04 Sensor
SG90 Servo
Sensor Pin | STM32 Pin
VCC | 5V
GND | GND
TRIG | PB0
ECHO | PB1 (Voltage Divider Req.)
Servo Pin | STM32 Pin
VCC | External 5V
GND | GND
Signal | PA6
STM32 Connections: Sensors & Actuators

## Slide 6
LED Status
Provides visual indication of the system's active alarm state.
Anode (+): PC0 (w/ 220Ω Resistor)
Cathode (-): GND
Active Buzzer
Provides high-decibel auditory alert upon unauthorized entry.
Positive (+): PC1
Negative (-): GND
Reset Button
Allows manual override or resetting the alarm state securely.
Pin 1: PC2
Pin 2: GND
STM32 Connections: Alarms & Inputs

## Slide 7
STM32 Pin | ESP32 Pin
PA2 (TX) | GPIO16 (RX2)
PA3 (RX) | GPIO17 (TX2)
GND | GND
Important Notes
• Connect Common Ground across boards.
• Add a 1kΩ resistor between STM32 TX & ESP32 RX to protect 3.3V logic.
• Standard Baud Rate: 115200
ESP32 to STM32 UART Connection

## Slide 8
1. Power ON
System boots up.
2. STM32 Init
Core setup complete.
3. Servo Locks
Door secured automatically.
4. Ultrasonic Scan
Object detected in range.
5. Threshold Check
Is Distance < Threshold? (YES)
System Workflow: Detection Phase

## Slide 9
1. Alarm Triggered
LED ON, Buzzer ON, Door Locked.
2. UART Sent
STM32 pushes alert to ESP32.
3. Cloud Update
Telegram & Firebase notified.
4. Owner Alert
Push notification received.
5. Remote Reset
Owner secures & unlocks via app.
System Workflow: Alert Phase

## Slide 10
UART Command Lexicon
STM32 UART Bridge ESP32 Firebase & Telegram
INTRUDER → Flags unauthorized entry
STATUS → Requests current system state
RESET → Turns off alarms & clears flags
LOCK → Engages servo lock mechanism
UNLOCK → Disengages servo lock
ESP32 & STM32 Communication

## Slide 11
Step 1
Navigate to the official Firebase console:
https://console.firebase.google.com
Step 2
Create a New Project.
Enable Google Analytics (Optional, but recommended for debugging). Click Continue.
Step 3
Open Realtime Database.
Click "Create Database" and select Test Mode to allow ESP32 read/write access.
Firebase Setup: Initial Configuration

## Slide 12
Step 4
Copy the Database URL.
Step 5
Go to Project Settings → Service Accounts.
Locate and copy the Database Secret / API Key.
Step 6
Open the ESP32 Code in Arduino IDE.
Replace FIREBASE_HOST and API_KEY with your copied credentials.
Firebase Setup: Integration Keys

## Slide 13
Status
"Locked"
Intruder
TRUE
Time
"10:30 PM"
Distance
"18 cm"
Firebase Data Structure

## Slide 14
Steps 1 & 2: Initiation
Step 1: Open the Telegram app and search for the official @BotFather.
Step 2: Type the command /newbot to initiate the creation process.
Steps 3 & 4: Credentials
Step 3: Enter a friendly Bot Name, followed by a unique Bot Username.
Step 4: BotFather will generate an HTTP API Token (BOT TOKEN). Copy and secure this token.
Telegram Bot Setup: Creation

## Slide 15
Steps 5 & 6
Step 5: Search your newly created Bot in Telegram and click START.
Step 6: Open a browser to:
api.telegram.org/botYOUR_TOKEN/getUpdates
Steps 7 & 8
Step 7: Send "Hello" to your bot in the app. Refresh the browser page.
Step 8: In the JSON response, locate the chat object and find the id. Copy this CHAT_ID.
Step 9
Integration: Open your ESP32 Code.
Paste the copied values into the BOT_TOKEN and CHAT_ID macros to link the hardware.
Telegram Bot Setup: Activation

## Slide 16
Command | System Action Triggered
/status | Returns the Current Status (Locked, Safe, Intrusion)
/reset | Remotely Resets Alarm and clears intrusion flags
/unlock | Manually Unlocks the Door via servo actuation
/lock | Manually Locks the Door securely
/arm | Arms Security mode & activates sensor polling
Telegram Commands

## Slide 17
Ultrasonic Sensor STM32 Controller Servo + LED + Buzzer Action UART Bridge ESP32 Module WiFi Router Firebase / Telegram API Owner Mobile Device
Complete Data Flow

## Slide 18
Automatic Intruder Detection Immediate sensing without blind spots.
Instant Telegram Alerts Notification delivered within milliseconds.
Cloud Monitoring Persistent logging in Firebase Database.
Remote Door Control App-based lock/unlock operations.
Real-Time Logging Track historical entry data accurately.
Low Cost Highly affordable off-the-shelf components.
Easy Installation Plug-and-play architectural design.
Expandable IoT System Open for additional smart sensors.
System Advantages

## Slide 19
Biometrics
Face Recognition & Fingerprint Authentication for secure local access.
Surveillance
ESP32-CAM module for live camera streaming inside the application.
Custom App
Dedicated Mobile Application Dashboard for unified control.
Voice Control
Integration with Voice Assistants (Alexa/Google Home).
RFID
Secure RFID card or tag-based access control logging.
AI Defense
AI-Based Intrusion Detection to reduce false positive alerts.
Future Enhancements

## Slide 20
Thank You!
Questions & Answers
STM32 + ESP32 + Firebase + Telegram